## Slide 1: MicroPython IOT 入門
Speaker: Jumbo
email: jumbokh@gmail.com

## Slide 2: Agenda
ESP32-s: MicroPython Firmware
Sensor: DHT11
MQTT How to
Monitor with APP @ Phone
Control a light or switch
Draw a Chart
More about MQTT
https://goo.gl/ciQ8rw

## Slide 3: 1. ESP32-S: MicroPython Firmware
Let’s start with the first set of slides

## Slide 4: Flash firmware
參考文章
下載Firmware:
http://micropython.org/download#esp32
先Erase：
esptool.py --port com12 erase_flash
再燒錄：
esptool --port com4 --chip esp32 write_flash -z 0x1000 esp32-idf3-20191202-v1.11-611-g7f24c2977.bin
(32m-->32Mb-->4MB)

## Slide 5: After flash fw.
esptool.py --port com12 flash_id
esptool.py v1.3
Connecting....
Manufacturer: e0
Device: 4016
esptool.py --port com12 chip_id
esptool.py v1.3
Connecting....
Chip ID: 0x00a3c7f0
Notes: 燒錄指令：
esptool.py --port com12 --baud 460800 write_flash --flash_size=detect -fm dio 0 py-esp8266-20170108-v1.8.7.bin
以下為過程的訊息，32m-->32Mb-->4MB
esptool.py v1.3
Connecting....
Auto-detected Flash size: 32m
Running Cesanta flasher stub...
Flash params set to 0x0240
Wrote 589824 bytes at 0x0 in 13.2 seconds (357.5 kbit/s)...
Leaving...

## Slide 6: Hello World with GPIO
Hello World MicroPython :
舊版可用p.low(), p.high()，新版只能用.value()
import machine
import time
p = machine.Pin(2, machine.Pin.OUT)
for i in range(6):
p.value(not p.value())
time.sleep(1)
DEMO:
hello-gpio.py

## Slide 7: ampy: 透過serial操作的好工具
說明頁面：adafruit-ampy
How to install: pip install adafruit-ampy
put script into board: ampy --port com12 put test.py ampy --port com12 put dir2
Run code: ampy --port com12 run test.py
Run code forever but no waiting ampy --port com12 run test2.py --no-output

## Slide 8: ampy: 透過serial操作的好工具
Reset ESP32-S ampy --port com12 reset
List files ampy --port com12 ls ampy --port com12 ls dir2
Make dir ampy --port com12 mkdir dir3
Remove dir ampy --port com12 rmdir dir3
Remove file ampy --port com12 rm data.txt

## Slide 9: ampy: 透過serial操作的好工具
get script from board: ampy --port com12 get boot.py Get boot.py, and then save as my-boot.py on PC ampy --port com12 get boot.py my-boot.py

## Slide 12: 2. Sensor: DHT-11

## Slide 13: DHT-11 (溫溼度sensor)
import dht import machine d = dht.DHT11(machine.Pin(4)) d.measure() d.temperature() # eg. 23 (°C) d.humidity() # eg. 41 (% RH) d = dht.DHT22(machine.Pin(4)) d.measure() d.temperature() # eg. 23.6 (°C) d.humidity() # eg. 41.3 (% RH)
DEMO:
dht11.py
Notes: https://akizukidenshi.com/download/ds/aosong/DHT11.pdf

## Slide 14: DHT-11 (溫溼度sensor)
DEMO:
dht11.py
Ref: https://akizukidenshi.com/download/ds/aosong/DHT11.pdf

## Slide 15: 3. MQTT How to

## Slide 16: MQTT
MQTT (Message Queue Telemetry Transport)
為M2M, IOT設計的協定，基於TCP socket，主要是想讓系統資源較低的設備也可以把資料上傳到Server。
目前已是ISO的一員 2016, MQTT is now an ISO standard (ISO/IEC 20922)
此處使用的MQTT雲端為Eclipse所提供： iot.eclipse.org
DEMO:
mq-dht11.py

## Slide 17: MQTT
來源網址

## Slide 18: MQTT Demo 執行前先修改的部份
TOPIC_BASE = 'iot/home2' 改為你自己的topic名稱
server = "iot.eclipse.org" 若有自己的MQTT Broker請俢改此行
wlan.connect(‘SSID', ‘Key') 依現場的網路修改帳密
其它的免費的MQTT： iot.eclipse.org test.mosquitto.org broker.hivemq.com cloudMqtt (要申請)
DEMO:
mq-dht11.py

## Slide 19: 4. Monitor with APP @ Phone

## Slide 20: MQTT
使用手機為Android手機 (iPhone我沒有，因此沒試過)
請安裝MQTT Dashboard這個APP。

## Slide 21: MQTT
(1)裝好後按+新增一個project
(2)填入Server, Port訊息 Client ID任意填
(1)
(2)

## Slide 22: MQTT
(3)按+新增一個訂閱(Subscript)的 主題(Topic)
(4)填入如圖的內容
新增完成畫面如下
(2)
(3)
(4)

## Slide 23: MQTT
按+新增一個訂閱(Subscript)的 主題(Topic)
(5)填入如圖的內容
將得到如圖的畫面
(5)

## Slide 24: 5. Control a light or switch
Let’s start with the first set of slides

## Slide 25: MQTT
(6)按+新增一個public的 主題(Topic)
(7)選擇Switch
(6)
(7)

## Slide 26: MQTT
(8)填入內容如圖
可以得到畫面如下
點switch可以控制ESP上的燈號
(7)

## Slide 27: 6. Make a chart
Let’s start with the first set of slides

## Slide 28: Make a chart
安裝Linear MQTT Dashboard。
操作如圖所示
(1)
(3)
(2)
(5)
(4)

## Slide 29: 7. More about MQTT
Let’s start with the first set of slides

## Slide 30: 漏掉資料?
在Broker的Server上同時有MQTT Client訂閱topic，直接放到DB中
把qos level提升

## Slide 31: THANKS!
Any questions?
You can find me at jumbokh@gmail.com